## Slide 1: SOC Design Lab
Lab4-0 – Caravel SOC Simulation
Jiin Lai

## Slide 2: Background
Caravel SOC Introduction - Refer to
PPT: hkust-soc-lab/Lab4/caravel-soc-ppt at main · roo-nju/hkust-soc-lab (github.com)
Youtube Channel: https://youtube.com/playlist?list=PL5CoDA0gtOHVeF4FkotwDY-buLVIoeGzf&si=teFjiOvwbZWLZboe

## Slide 3: Caravel Simulation Verification System
Verilog testbench
counter_la_tb.v
Module counter_tb;
Initial beigin
wait(checkbits == 16’hAB40);
wait(checkbits = ..
End
Initial begin
RSB <= 1’b0;
RSB <= 1’b1;
end
Caravel uut( );
Spiflash #( .FILENAME(“counter_la.hex”} spiflash ( );
tbuart tburat ( );
endmodule

## Slide 4: Bring up Caravel SOC Simulation
Refer to the Github to bring up Caravel SOC simulation
  https://github.com/bol-edu/caravel-soc (iverilog)
  Follow the following step to bring up the Toolchain
    https://github.com/bol-edu/caravel-soc#toolchain-prerequisites
    Follow the following step to use Xilinx XSIM
    https://github.com/bol-edu/caravel-soc_fpga#run-xilinx-vivado-simulation-of-caravel-soc-fpga (Xsim)
      git clone https://github.com/bol-edu/caravel-soc_fpga
      Follow the link: https://github.com/bol-edu/caravel-soc_fpga#run-xilinx-vivado-simulation-of-caravel-soc-fpga
      Execute the xsim example
Run the following example
  counter_la, coutner_wb, gcd_la

## Slide 5: Observe and Learn the following
Observe the following
  spiflash access & code execution (observe CPU trace )
  cpu wb cycles interaction with user project area.
  cpu interface with user project with la
  User project/RISC-V uses mprj pin, and interacts with Testbench
Learn the following
  RISC-V tool chain
  Caravel testbench structure
  Caravel SOC design
  RISC-V firmware development
  User project integrates with Caravel SOC
  GDB + GDBWave Debugging (caravel-soc, iverilog) - (optional )
  Trace Verilog code with Vim + vtags (caravel-soc, iverilog) – ( optional )
  Using CPU trace ( https://github.com/bol-edu/caravel-soc/tree/cpu-trace ) - caravel-soc, iverilog (optional)

## Slide 6: You do not need to turn-in report This is for you to prepare Lab4-1, Lab4-2